## Slide 1
Saturation Flow
2023
GROUP NO : 4
Participant's:
  Md Arid Ishtiaq (20105061)
  Usayed Islam (20105062)
  Mahmudul Hassan Tamim (20105051)
  Raiyan Ferdous (20105052)
  Md. Khairul Amin (20105065)
  Md. Atif Aziz (20105066)

## Slide 2: INTRODUCTION
Definition of saturation flow:
The maximum flow that can be discharged from a traffic lane when there is a continuous green indication and a continuous queue on the approach.
Saturation Flow
2023

## Slide 3: INTRODUCTION
Saturation Flow
2023
Importance of saturation flow in traffic engineering
Measure the maximum rate of flow of traffic.
Used intersection control and design.
A critical parameter as it directly influences the capacity of an intersection
To determine number of lanes
the duration of green and red phases
overall capacity of a roadway segment

## Slide 4: Factors Affecting Saturation Flow
Numbers of Lanes
Lane width
Intersection geometry
Pedestrian activity
Signal timing

## Slide 5: Calculation
Saturation Flow
2023
𝑆𝑎𝑡𝑢𝑟𝑎𝑡𝑖𝑜𝑛 𝑓𝑙𝑜𝑤, 𝑆
=
(20.89+27.87)
2
= 24.43 PCU per 30 sec
= 0.8143 PCU per sec
(24.43/30)
= 2931.6 PCU per hour
(0.8143*3600)

## Slide 6: Calculation: Initial Lost time
Saturation Flow
2023
Initial Lost time:
𝑛𝑖
𝑠
𝑙𝑖 = 𝑡𝑖 −
= 30 sec −
27.16 𝑷𝑪𝑼
0.8143 𝑷𝑪𝑼/𝒔𝒆𝒄
= − 3.35 sec
= assume 3.35 sec

## Slide 7: Calculation: Final Lost Time
Saturation Flow
2023
Methods for calculating saturation flow (e.g., HCM method)
Data required for calculation (e.g., lane width, demand volume, green time)
Final Lost time:
𝑙𝑓 = 𝑡𝑓 −
= 30 sec −
𝑛𝑓
𝑠
20.34 𝑃𝐶𝑈
0.8143 𝑷𝑪𝑼/𝒔𝒆𝒄
= 5.02 sec

## Slide 8: Calculation: Effective Green TIme
Saturation Flow
2023
𝑔 = 𝐺 + 𝐴 − (𝑙𝑖 + 𝑙𝑓)
= 120 sec − (3.35 + 5.02)
= 111.63 sec

## Slide 9: Calculation: Approch Capacity
Saturation Flow
2023
𝑎𝑝𝑝𝑟𝑜𝑎𝑐ℎ 𝑐𝑎𝑝𝑎𝑐𝑖𝑡𝑦 =
𝐶
𝑔 𝑥 𝑆 [C = G+A+R]
=
120 𝑠𝑒𝑐
360 𝑠𝑒𝑐
𝑥 2931.6
= 977.2 𝑃𝐶𝑈/ℎ𝑟
𝑨𝒔𝒔𝒖𝒎𝒊𝒏𝒈 𝑪𝒚𝒄𝒍𝒆 𝒍𝒆𝒏𝒈𝒕𝒉 = 𝟔𝟎 𝒔𝒆𝒄

## Slide 10: Diagram
Saturation Flow
2023
Chart: Saturation Flow Diagram
| Vehicle
0-30 | 27.16
30-60 | 20.89
60-90 | 27.97
90-120 | 20.34

## Slide 11: Example Calculation
Demonstration of how to calculate saturation flow using the HCM method
Input data and assumptions
Results and
interpretation

## Slide 12: Importance of Saturation Flow in Signal Timing How saturation flow is used in signal timing
Benefits of optimizing signal timing based on saturation flow

## Slide 13: Saturation Flow and Sustainable Transportation
Importance of saturation flow in promoting sustainable transportation (e.g., reducing emissions and congestion)
Importance of saturation flow in promoting sustainable transportation (e.g., reducing emissions and congestion)

## Slide 14: Conclusion
2023
Intersection capacity
Optimizing signal timing
Promoting sustainable transportation
Saturation Flow
Saturation flow is essential to determine
By considering saturation flow we can,
Reduce traffic congestion ,emission ,travel time
Reduce the rate of accidents.
Enhance safety for all users.

## Slide 15
THANKS!
DO YOU HAVE ANY QUESTIONS?